AGRO 6997 Applications in Remote Sensing

Assignment No. 2

Feb 6, 2012

Objective: Comparison of the average January 2012 reference evapotranspiration  (ETo) estimated using the Hargraves Samini, Priestly Taylor and Penman Monteith methods.

Steps:

- Start with your program from Assignment No. 1

- Download the file for the average January 2012 wind speed from the website: http://academic.uprm.edu/hdc/6997/ASSIGNMENT_2/

- Estimate the Net Radiation using the equation given in reading.  A detailed description is provided in this week’s reading:   http://www.fao.org/docrep/X0490E/x0490e07.htm#solar%20radiation

- Estimate the climatological parameters using the equations given in the appendix (Tmin, Tmax, es, ea, Δ, gamma)

- Plot Tmin, Tmax, es, ea, Δ, gamma

- Plot Penman-Monteith and Priestly-Tailor ETo.

- Compare the three methods for estimating ETo.

- Please submit a short report with all graphics two weeks from tonight.  We will work on this problem in the computer lab tonight and next Monday night.

Appendix

CLIMATE PARAMETERS

1. Four principle climate parameters

- Solar Radiation

- Air Temperature

- Humidity

- Wind Speed

RADIATION

Standard unit: megajoule per square metre and per day (MJ m-2 day-1) or as equivalent evaporation in mm per day (mm day-1)

| equivalent evaporation (mm/day) | 1 mm day-1 = 2.45 MJ m-2 day-1 |
| --- | --- |
| joule per cm2 per day (J cm-2 day-1) | 1 J cm-2 day-1 = 0.01 MJ m-2 day-1 |
| calorie per cm2 per day (cal cm-2 day-1) | 1 cal = 4.1868 J = 4.1868 10-6 MJ |
|  | 1 cal cm-2 day-1 = 4.1868 10-2 MJ m-2 day-1 |
| watt per m2 (W m-2) | 1 W = 1 J s-1 |
|  | 1 W m-2 = 0.0864 MJ m-2 day-1 |

TEMPERATURE

Standard unit: degree Celsius (°C)

| degree Fahrenheit (°F) | (°C) = (°F-32) 5/9 |
| --- | --- |
| Kelvin (K) | 1K = (°C) + 273.16 |

PRESSURE (air pressure, vapour pressure)

Standard unit: kilopascal (kPa)

| millibar (mbar) | 1 mbar = 0.1 kPa |
| --- | --- |
| bar | 1bar = 100 kPa |
| centimetre of water (cm) | 1 cm of water = 0.09807 kPa |
| millimetre of mercury (mmHg) | 1 mmHg = 0.1333 kPa |
| atmospheres (atm) | 1 atm = 101.325 kPa |
| pound per square inch (psi) | 1 psi = 6.896 kPa |

WIND SPEED

Standard unit: metre per second (m s-1)

| kilometre per day (km day-1) | 1 km day-1 = 0.01157 m s-1 |
| --- | --- |
| nautical mile/hour (knot) | 1 knot = 0.5144 m s-1 |
| foot per second (ft s-1) | 1 ft/s = 0.3048 m s-1 |

To describe the principle climate parameters we need to use various equations.

Air Pressure

P = Air Pressure (kPa)

z = Elevation above mean sea level (m)

Atmospheric pressure (P) for different altitudes (z)

| (Eq. 7) |
| --- |
| z (m) | P (kPa) | z (m) | P (kPa) | z (m) | P (kPa) | z (m) | P (kPa) |
| 0 | 101.3 | 1000 | 90.0 | 2000 | 79.8 | 3000 | 70.5 |
| 50 | 100.7 | 1050 | 89.5 | 2050 | 79.3 | 3050 | 70.1 |
| 100 | 100.1 | 1100 | 89.0 | 2100 | 78.8 | 3100 | 69.6 |
| 150 | 99.5 | 1150 | 88.4 | 2150 | 78.3 | 3150 | 69.2 |
| 200 | 99.0 | 1200 | 87.9 | 2200 | 77.9 | 3200 | 68.8 |
| 250 | 98.4 | 1250 | 87.4 | 2250 | 77.4 | 3250 | 68.3 |
| 300 | 97.8 | 1300 | 86.8 | 2300 | 76.9 | 3300 | 67.9 |
| 350 | 97.2 | 1350 | 86.3 | 2350 | 76.4 | 3350 | 67.5 |
| 400 | 96.7 | 1400 | 85.8 | 2400 | 76.0 | 3400 | 67.1 |
| 450 | 96.1 | 1450 | 85.3. | 2450 | 75.5 | 3450 | 66.6 |
| 500 | 95.5 | 1500 | 84.8 | 2500 | 75.0 | 3500 | 66.2 |
| 550 | 95.0 | 1550 | 84.3 | 2550 | 74.6 | 3550 | 65.8 |
| 600 | 94.4 | 1600 | 83.8 | 2600 | 74.1 | 3600 | 65.4 |
| 650 | 93.8 | 1650 | 83.3 | 2650 | 73.7 | 3650 | 65.0 |
| 700 | 93.3 | 1700 | 82.8 | 2700 | 73.2 | 3700 | 64.6 |
| 750 | 92.7 | 1750 | 82.3 | 2750 | 72.7 | 3750 | 64.1 |
| 800 | 92.2 | 1800 | 81.8 | 2800 | 72.3 | 3800 | 63.7 |
| 850 | 91.6 | 1850 | 81.3 | 2850 | 71.8 | 3850 | 63.3 |
| 900 | 91.1 | 1900 | 80.8 | 2900 | 71.4 | 3900 | 62.9 |
| 950 | 90.6 | 1950 | 80.3 | 2950 | 71.0 | 3950 | 62.5 |
| 1000 | 90.0 | 2000 | 79.8 | 3000 | 70.5 | 4000 | 62.1 |

Latent Heat of Vaporization (λ)

The latent heat of vaporization is the amount of energy required to evaporate 1 kg of water = 2.45 MJ/kg.  This parameter is a function of temperature.  The above value is for a temperature of 20 oC, which is sufficiently accurate for most calculations.

Psychometric Constant

Psychometric constant () for different altitudes (z)   (MULTIPLY 0.664E-3 BY P)

| (Eq. 8) |
| --- |
| z (m) |  kPa/°C | z (m) |  kPa/°C | z (m) |  kPa/°C | z (m) |  kPa/°C |
| 0 | 0.067 | 1000 | 0.060 | 2000 | 0.053 | 3000 | 0.047 |
| 100 | 0.067 | 1100 | 0.059 | 2100 | 0.052 | 3100 | 0.046 |
| 200 | 0.066 | 1200 | 0.058 | 2200 | 0.052 | 3200 | 0.046 |
| 300 | 0.065 | 1300 | 0.058 | 2300 | 0.051 | 3300 | 0.045 |
| 400 | 0.064 | 1400 | 0.057 | 2400 | 0.051 | 3400 | 0.045 |
| 500 | 0.064 | 1500 | 0.056 | 2500 | 0.050 | 3500 | 0.044 |
| 600 | 0.063 | 1600 | 0.056 | 2600 | 0.049 | 3600 | 0.043 |
| 700 | 0.062 | 1700 | 0.055 | 2700 | 0.049 | 3700 | 0.043 |
| 800 | 0.061 | 1800 | 0.054 | 2800 | 0.048 | 3800 | 0.042 |
| 900 | 0.061 | 1900 | 0.054 | 2900 | 0.047 | 3900 | 0.042 |
| 1000 | 0.060 | 2000 | 0.053 | 3000 | 0.047 | 4000 | 0.041 |

The above table is based on:

λ = 2.45 MJ kg-1,

cp specific heat at constant pressure,

1.013 10-3 [MJ kg-1 °C-1],

ε ratio molecular weight of water vapour/dry air = 0.622.

Temperature = 20°C

The specific heat (cp) at constant pressure is the amount of energy required to increase the temperature of a unit mass of air by one degree at constant pressure. Its value depends on the composition of the air, i.e., on its humidity. For average atmospheric conditions a value cp = 1.013 10-3 MJ kg-1 °C-1 can be used. As an average atmospheric pressure is used for each location (Eq. 7), the psychrometric constant (Eq. 8) is kept constant for each location.

2. Air Temperature

- Measured inside shelters at 2 m above the ground.

- Air temperature is measured with thermometers, thermistors or thermocouples mounted in the shelter

- Electronic weather stations often sample air temperature each minute and report hourly averages in addition to 24-hour maximum and minimum values.

- The daily maximum air temperature (Tmax) and daily minimum air temperature (Tmin) are, respectively, the maximum and minimum air temperature observed during the 24-hour period, beginning at midnight.

The average daily temperature Tmean for 24-hour periods is defined as the mean of the daily maximum (Tmax) and minimum temperatures (Tmin) rather than as the average of hourly temperature measurements:

Tmean = (Tmax + Tmin)/2 								(9)

The temperature is given in degrees Celsius (°C) or Fahrenheit (°F).

In some calculation procedures, temperature is required in Kelvin (K), which can be obtained by adding 273.16 to the temperature expressed in degrees Celsius (in practice K = °C + 273.16). The Kelvin and Celsius scale have the same scale interval.

3. Air Humidity

Concept:  The water content of the air can be expressed in several ways. In agrometeorology, vapor pressure, dewpoint temperature and relative humidity are common expressions to indicate air humidity.

Vapor Pressure

- Water vapor is a gas

- The water vapor pressure contributes to the total atmospheric pressure

- The amount of water vapor in the air is related directly to the partial pressure exerted by the water vapor

Saturation vapor pressure e°(T)

- When air is enclosed over saturated liquid water, the air becomes saturated with water vapor.

- The corresponding vapor pressure is called the saturated vapor pressure.

- The amount of vapor the air can hold depends on its temperature. (higher temperature air can hold more water).  Therefore, the saturated vapor pressure is dependent on air temperature.

Saturation vapor pressure shown as a function of temperature: e°(T) curve

The saturation vapor pressure at temperature T is given by the following equation:

(11)

where

e°(T) saturation vapour pressure at the air temperature T [kPa],
T air temperature [°C],
exp[..] 2.7183 (base of natural logarithm) raised to the power [..].

The saturated vapor pressure can also be obtained from the following table:

Saturation vapour pressure (e°(T)) for different temperatures (T)

| (Eq. 11) |
| --- |
| T °C | es kPa | T °C | e°(T) kPa | T °C | e°(T) kPa | T °C | es kPa |
| 1.0 | 0.657 | 13.0 | 1.498 | 25.0 | 3.168 | 37.0 | 6.275 |
| 1.5 | 0.681 | 13.5 | 1.547 | 25.5 | 3.263 | 37.5 | 6.448 |
| 2.0 | 0.706 | 14.0 | 1.599 | 26.0 | 3.361 | 38.0 | 6.625 |
| 2.5 | 0.731 | 14.5 | 1.651 | 26.5 | 3.462 | 38.5 | 6.806 |
| 3.0 | 0.758 | 15.0 | 1.705 | 27.0 | 3.565 | 39.0 | 6.991 |
| 3.5 | 0.785 | 15.5 | 1.761 | 27.5 | 3.671 | 39.5 | 7.181 |
| 4.0 | 0.813 | 16.0 | 1.818 | 28.0 | 3.780 | 40.0 | 7.376 |
| 4.5 | 0.842 | 16.5 | 1.877 | 28.5 | 3.891 | 40.5 | 7.574 |
| 5.0 | 0.872 | 17.0 | 1.938 | 29.0 | 4.006 | 41.0 | 7.778 |
| 5.5 | 0.903 | 17.5 | 2.000 | 29.5 | 4.123 | 41.5 | 7.986 |
| 6.0 | 0.935 | 18.0 | 2.064 | 30.0 | 4.243 | 42.0 | 8.199 |
| 6.5 | 0.968 | 18.5 | 2.130 | 30.5 | 4.366 | 42.5 | 8.417 |
| 7.0 | 1.002 | 19.0 | 2.197 | 31.0 | 4.493 | 43.0 | 8.640 |
| 7.5 | 1.037 | 19.5 | 2.267 | 31.5 | 4.622 | 43.5 | 8.867 |
| 8.0 | 1.073 | 20.0 | 2.338 | 32.0 | 4.755 | 44.0 | 9.101 |
| 8.5 | 1.110 | 20.5 | 2.412 | 32.5 | 4.891 | 44.5 | 9.339 |
| 9.0 | 1.148 | 21.0 | 2.487 | 33.0 | 5.030 | 45.0 | 9.582 |
| 9.5 | 1.187 | 21.5 | 2.564 | 33.5 | 5.173 | 45.5 | 9.832 |
| 10.0 | 1.228 | 22.0 | 2.644 | 34.0 | 5.319 | 46.0 | 10.086 |
| 10.5 | 1.270 | 22.5 | 2.726 | 34.5 | 5.469 | 46.5 | 10.347 |
| 11.0 | 1.313 | 23.0 | 2.809 | 35.0 | 5.623 | 47.0 | 10.613 |
| 11.5 | 1.357 | 23.5 | 2.896 | 35.5 | 5.780 | 47.5 | 10.885 |
| 12.0 | 1.403 | 24.0 | 2.984 | 36.0 | 5.941 | 48.0 | 11.163 |
| 12.5 | 1.449 | 24.5 | 3.075 | 36.5 | 6.106 | 48.5 | 11.447 |

The average daily saturated vapor pressure is given by

(12)

Actual vapor pressure (ea)

- The actual vapour pressure is the vapour pressure exerted by the water in the air.

- When the air is not saturated, the actual vapour pressure will be lower than the saturation vapour pressure.

- The difference between the saturation and actual vapour pressure is called the vapour pressure deficit or saturation deficit and is an accurate indicator of the actual evaporative capacity of the air.

Actual vapor pressure (ea) derived from dewpoint temperature

As the dewpoint temperature is the temperature to which the air needs to be cooled to make the air saturated, the actual vapor pressure (ea) is the saturation vapor pressure at the dewpoint temperature (Tdew) [°C], or:

(14)

Dewpoint Temperature (Tdew)

- The dewpoint temperature is the temperature to which the air needs to be cooled to make the air saturated.

- The actual vapor pressure of the air is the saturation vapor pressure at the dewpoint temperature.

- The drier the air, the larger the difference between the air temperature and dewpoint temperature.

Relative Humidity (RH)

- The relative humidity (RH) expresses the degree of saturation of the air as a ratio of the actual (ea) to the saturation (e°(T)) vapor pressure at the same temperature (T):

(10)

Example Calculation:  Calculated the average daily relative humidity for the following conditions:  Tmax = 30 oC, Tmin = 18oC, Tdew = 18 oC.

Slope of saturation vapour pressure curve ( )

For the calculation of evapotranspiration, the slope of the relationship between saturation vapour pressure and temperature, , is required.

(13)

where

 slope of saturation vapour pressure curve at air temperature T [kPa °C-1],
T air temperature [°C],
exp[..] 2.7183 (base of natural logarithm) raised to the power [..].

TABLE 2.4. Slope of vapour pressure curve () for different temperatures (T)

| (Eq. 13) |
| --- |
| T °C |  kPa/°C | T °C |  kPa/°C | T °C |  kPa/°C | T °C |  kPa/°C |
| 1.0 | 0.047 | 13.0 | 0.098 | 25.0 | 0.189 | 37.0 | 0.342 |
| 1.5 | 0.049 | 13.5 | 0.101 | 25.5 | 0.194 | 37.5 | 0.350 |
| 2.0 | 0.050 | 14.0 | 0.104 | 26.0 | 0.199 | 38.0 | 0.358 |
| 2.5 | 0.052 | 14.5 | 0.107 | 26.5 | 0.204 | 38.5 | 0.367 |
| 3.0 | 0.054 | 15.0 | 0.110 | 27.0 | 0.209 | 39.0 | 0.375 |
| 3.5 | 0.055 | 15.5 | 0.113 | 27.5 | 0.215 | 39.5 | 0.384 |
| 4.0 | 0.057 | 16.0 | 0.116 | 28.0 | 0.220 | 40.0 | 0.393 |
| 4.5 | 0.059 | 16.5 | 0.119 | 28.5 | 0.226 | 40.5 | 0.402 |
| 5.0 | 0.061 | 17.0 | 0.123 | 29.0 | 0.231 | 41.0 | 0.412 |
| 5.5 | 0.063 | 17.5 | 0.126 | 29.5 | 0.237 | 41.5 | 0.421 |
| 6.0 | 0.065 | 18.0 | 0.130 | 30.0 | 0.243 | 42.0 | 0.431 |
| 6.5 | 0.067 | 18.5 | 0.133 | 30.5 | 0.249 | 42.5 | 0.441 |
| 7.0 | 0.069 | 19.0 | 0.137 | 31.0 | 0.256 | 43.0 | 0.451 |
| 7.5 | 0.071 | 19.5 | 0.141 | 31.5 | 0.262 | 43.5 | 0.461 |
| 8.0 | 0.073 | 20.0 | 0.145 | 32.0 | 0.269 | 44.0 | 0.471 |
| 8.5 | 0.075 | 20.5 | 0.149 | 32.5 | 0.275 | 44.5 | 0.482 |
| 9.0 | 0.078 | 21.0 | 0.153 | 33.0 | 0.282 | 45.0 | 0.493 |
| 9.5 | 0.080 | 21.5 | 0.157 | 33.5 | 0.289 | 45.5 | 0.504 |
| 10.0 | 0.082 | 22.0 | 0.161 | 34.0 | 0.296 | 46.0 | 0.515 |
| 10.5 | 0.085 | 22.5 | 0.165 | 34.5 | 0.303 | 46.5 | 0.526 |
| 11.0 | 0.087 | 23.0 | 0.170 | 35.0 | 0.311 | 47.0 | 0.538 |
| 11.5 | 0.090 | 23.5 | 0.174 | 35.5 | 0.318 | 47.5 | 0.550 |
| 12.0 | 0.092 | 24.0 | 0.179 | 36.0 | 0.326 | 48.0 | 0.562 |
| 12.5 | 0.095 | 24.5 | 0.184 | 36.5 | 0.334 | 48.5 | 0.574 |