## Slide 1
Planificación de riego para ahorrar dinero, agua y energía
Dr. Eric Harmsen
Professor, Dept. of Agricultural and Biosystems Eng., Univ. of Puerto Rico-Mayaguez
Eric.harmsen@upr.edu
(787)955-5102
Taller de Riego
Juana Diaz, Puerto Rico, Marzo 12, 2014

## Slide 2: ACKNOWLEDGEMENT
Colegio de Ciencias Agrícolas, Universidad de Puerto Rico
Agro Servicios Inc.
USDA Hatch Project (H-402)
NOAA-CREST Project

## Slide 3: Irrigation Scheduling - What is the problem?
There is anecdotal evidence that most farmers do not use scientific methods for scheduling irrigation
Data from Idaho, USA
http://www.webpages.uidaho.edu/~karenl/wq/wqbr/wqbr26.html

## Slide 4: Definition
What is irrigation scheduling? Irrigation Scheduling is the process used by irrigation system managers (farmers) to determine the correct frequency and duration of watering. (wikipedia.org)

## Slide 5: Why do we care?
Over application of water
Leads to the waste of
  water
  energy
  chemicals
  money
  may lead to the contamination of ground and surface waters.
  leaching of fertilizers past the root zone
  water logging
  lower crop yields.
Under-application of water
Leads to
  crop water stress
  Reduced crop yield
  loss of revenue to the grower

## Slide 6: How much money are we talking about?
 | Relative Irrigation Applied |  |  |  |  |  | 
 | 0.4 | 0.5 | 0.8 | 1.0 | 1.3 | 1.5 | 1.8
Cultivo* | $ Lost / Cuerda |  |  |  |  |  | 
Gandules | 47 | 32 | 10 | 0 | 12 | 35 | 69
Pepinillo | 111 | 76 | 25 | 0 | 15 | 56 | 124
Repollo | 256 | 174 | 57 | 0 | 21 | 103 | 247
Sandia | 293 | 199 | 65 | 0 | 23 | 114 | 277
Platanos y Guineos, Plantilla | 318 | 216 | 71 | 0 | 24 | 122 | 299
Calabaza | 390 | 265 | 87 | 0 | 27 | 146 | 359
Cebolla | 543 | 369 | 121 | 0 | 34 | 195 | 490
Pimiento | 578 | 393 | 129 | 0 | 36 | 206 | 519
Barenjena | 757 | 514 | 169 | 0 | 44 | 264 | 670
Platanos y Guineos, Reton~o | 1,006 | 684 | 225 | 0 | 76 | 388 | 945
Melon, Cantaloupe y Honeydew | 1,027 | 698 | 229 | 0 | 56 | 352 | 899
Raices y Tuberculos | 1,041 | 707 | 232 | 0 | 57 | 356 | 911
    *Based model budget data from the Conjunto Tecnológico, UPR Experment Station

## Slide 7
Objective
To review several important soil and water concepts related to irrigation management
To introduce several methods of scheduling irrigation

## Slide 8: METHODS
Experience Method
Water Supply Method
Evapotranspiration Method
Soil Moisture Method
Water balance method

## Slide 9: Experience Method
“I apply 1 inch of water to my crop every week.”
“The soil looks dry so I am going to irrigate.”
“The crop looks stressed so I am going to irrigate.”

## Slide 10: Water Supply Method
The farm receives a certain amount of water on dates that are already fixed in advance.
The method takes into account the average rainfall only and thus does not take into account the actual rainfall;
this results in over-irrigation in wetter than average years and under-irrigation in drier than average years.
This method is commonly used with surface irrigation systems.
http://www.fao.org/docrep/t7202e/t7202e06.htm

## Slide 11: Evapotranspiration (ET) Method 1. Simple method (if you are currently not doing anything). http://www.fao.org/docrep/s2022e/s2022e02.htm

## Slide 12
Chart: Cumulative ETc vs. Irrigation

## Slide 13
TABLE 1. AVERAGE DAILY WATER NEEDS (MM) OF
STANDARD GRASS DURING IRRIGATION SEASON

## Slide 14
CROP WATER NEEDS IN PEAK PERIOD OF VARIOUS FIELD CROPS AS COMPARED TO STANDARD GRASS

## Slide 15
http://www.ianrpubs.unl.edu/epublic/live/g1994/build/graphics/g1994-2.jpg

## Slide 16: Example of simple ET method
Crop: Sugar cane
Location: Aguada, Puerto Rico
Area: 50 cuerda
Determine the irrigation requirement for one week during the peak of the growing season.
Pump flow rate is 1000 gpm
Assume irrigation system is 75% efficient

## Slide 17
TABLE 1. AVERAGE DAILY WATER NEEDS (MM) OF
STANDARD GRASS DURING IRRIGATION SEASON

## Slide 18
CROP WATER NEEDS IN PEAK PERIOD OF VARIOUS FIELD CROPS AS COMPARED TO STANDARD GRASS

## Slide 19: Calculations
From Table 1: Water need for standard grass is 7 mm
From table 2: add 20%.
  1.2 x 7 mm/day x 7 days = 59 mm
Calculate total gallons:
  59 mm x 50 cuerda x 1044 / 0.75
  = 4,090,000 million gallons
Pumping time:
  4,090,000 gal/1000 gal/min *60 min/hr = 68 hours

## Slide 20: Evapotranspiration Method 2. Web-based ET method
http://pragwater.com/daily-reference-evapotranspiration-eto-for-puerto-rico-hispaniola-and-jamaica/

## Slide 21
http://pragwater.com/2012/03/29/simple-irrigation-scheduling-tool-for-puerto-rico/

## Slide 22: Web-based method for irrigation scheduling in PR
Define problem (location, farm size, crop, etc.)
Determine ETo
Determine rainfall
from onsite gauge or NEXRAD
Estimate Crop Water Requirement
ETc = Kc ETo
Determine average Kc for the time period
Estimate Irrigation Requirement and required hours of pumping
Start
Harmsen E.W., 2012. TECHNICAL NOTE: A Simple Web-Based Method for Scheduling Irrigation in Puerto Rico J. Agric. Univ. P.R. 96 (3-4) 2012.

## Slide 23: Detailed Example
Determine the irrigation requirement for the 5 day period, February 15-19, 2012, for a tomato crop in Juana Diaz, Puerto Rico.
Required Hyperlinks
Length of Growth Stages (Table 11) and Crop Coefficients (Table 12) | http://www.fao.org/docrep/X0490E/x0490e00.htm
Daily Reference Evapotranspiration (ETo) | http://academic.uprm.edu/hdc/GOES-PRWEB_RESULTS/rainfall
Daily NEXRAD Rainfall for Puerto Rico | http://academic.uprm.edu/hdc/GOES-PRWEB_RESULTS/reference_ET/

## Slide 24
Step 1. Information used in example problem.

## Slide 25
Step 2. Crop growth stage and crop coefficient data for example problem.
http://www.fao.org/docrep/X0490E/x0490e00.htm
Tomato Growth Stages and Crop Coefficients

## Slide 26: Crop Coefficient
The averge Kc value of 0.85 for the five day period was obtained.
Crop coefficient curve for the example problem. The heavy dashed line applies to the example problem with day of season 46-50 (i.e., Feb 15-19) corresponding to an approximate crop coefficient of 0.85 (vertical axis).

## Slide 27: Step 3. Rainfallhttp://academic.uprm.edu/hdc/GOES-PRWEB_RESULTS/rainfall/
Inspection of the rainfall maps at the URL provided indicates that there was no rainfall during the five day period.

## Slide 28: Step 4. Reference Evapotranspiration (ETo) http://academic.uprm.edu/hdc/GOES-PRWEB_RESULTS/reference_ET/
Inspection of the ETo maps at the URL provided above indicates that there was 16.1 mm of ETo during the five day period.

## Slide 29: Step 5. Crop Water Requirement
The crop water requirement (ETc) for the five day period can now be estimated as follows:
ETc = Kc ETo = (0.85)(16.1 mm) = 13. 7 mm

## Slide 30: Step 6. Calculation of Irrigation Requirement and duration of pumping
Using D = ETc = 13.7 mm
A = 10 acres
Q = 300 gallons per minute
eff = 0.85, yields:
Irrigation Requirement (volume)
13.7 mm x 10 cuerda x 1044 / 0.85
  = 168,260 gallons
Pumping time:
168,260 gal/300 gal/min *60 min/hr = 9.35 hours

## Slide 31: Web-based Irrigation Scheduling Tool
Students from the Computer Engineering Department are developing desktop and mobile apps of the web-based irrigation scheduling procedure.
The user will be able to create an account, which will remember the user irrigation history
Everything will be automated
The apps should be ready for use in approximately 3 months.

## Slide 32: Puerto Rico Evapotranspiration Computer Program
http://pragwater.com/crop-water-use/

## Slide 33: PRET

## Slide 34: Soil Moisture Methods
Maintain soil water between
θFC and θt

## Slide 35: Soil Water Reservoir
AIR VOLUME
WATER VOLUME
SOLID VOLUME

## Slide 36: Water Volume
DRAINABLE WATER
TOTAL
AVAILABLE WATER
IMMOBILE
WATER

## Slide 37: Total Available Water
READILY
AVAILABLE
WATER
TOTAL
AVAILABLE
WATER

## Slide 38: The Soil Water Characteristic Curve
Volumetric Soil Moisture Content (θ)
Soil Water
Pressure
TOTAL AVAILABLE WATER

## Slide 39: Total Available Water
TAW = θFC - θWP
where
θFC = Volumetric moisture content a the field capacity
θWP = Wilting point volumetric moisture content.

## Slide 40: Representative Physical Properties of Soils

## Slide 41: The Soil Water Characteristic Curve
Volumetric Soil Moisture Content (θ)
Soil Water
Pressure
RAW
Threshold

## Slide 42: Readily Available Water
Plants can only remove a portion of the available water before growth and yield are affected. This portion is the “readily available water” (RAW).
For most crops RAW is between 20% to 65%
RAW is estimated from the following formula:
RAW = (MAD) (TAW)

## Slide 43: Management Allowed Deficit (MAD)
MAD

## Slide 44: Threshold Moisture Content, θt
If the soil moisture content falls below θt , the crop will go into stress and you will loss crop yield!
θt = θFC – RAW
where
θt = threshold moisture content
θFC = field capacity moisture content
RAW = readily available water

## Slide 45: The Soil Water Characteristic Curve
Volumetric Soil Moisture Content (θ)
Soil Water
Pressure
Threshold
STRESS
NO
STRESS
LOST

## Slide 46
Maintain soil water between
θFC and θt

## Slide 47: Soil Moisture Method
Perhaps the best method because it considers the readily available water in the soil.
Gravimetric method
Tensiometers
Electrical method
Water balance method

## Slide 48: Gravimetric Soil Sampling

## Slide 49: Tensiometers

## Slide 50: TDR
Time Domain Reflectometry

## Slide 51: Capacitance Method

## Slide 52
Maintain soil water between
θFC and θt

## Slide 53: Water Balance Method
θt2 = R + Irr – RO – ETc adj – PERC + θt1
θt2 = volumetric moisture content at time 2
θt1 = volumetric moisture content at time 1
R = effective rainfall
RO = runoff
PERC = water that percolates past the root zone

## Slide 54
http://pragwater.com/2011/12/17/a-simple-irrigation-scheduling-spreadsheet-program/

## Slide 55: Soil Water Management Spreadsheet
http://pragwater.com/2011/12/17/a-simple-irrigation-scheduling-spreadsheet-program/
User must enter the yellow spreadsheet cells

## Slide 58
Chart: Crop Stress Factor Vs. Time
| 39521.0 | 39522.0 | 39523.0 | 39524.0 | 39525.0 | 39526.0 | 39527.0 | 39528.0 | 39529.0 | 39530.0 | 39531.0 | 39532.0 | 39533.0 | 39534.0 | 39535.0 | 39536.0 | 39537.0 | 39538.0 | 39539.0 | 39540.0 | 39541.0 | 39542.0 | 39543.0 | 39544.0 | 39545.0 | 39546.0 | 39547.0 | 39548.0 | 39549.0
 | 1 | 1 | 1 | 0.9632 | 0.91499 | 0.86755 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.98004 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 60
Chart: Soil Moisture Content Vs. Date
| 39521.0 | 39522.0 | 39523.0 | 39524.0 | 39525.0 | 39526.0 | 39527.0 | 39528.0 | 39529.0 | 39530.0 | 39531.0 | 39532.0 | 39533.0 | 39534.0 | 39535.0 | 39536.0 | 39537.0 | 39538.0 | 39539.0 | 39540.0 | 39541.0 | 39542.0 | 39543.0 | 39544.0 | 39545.0 | 39546.0 | 39547.0 | 39548.0 | 39549.0
 | 30 | 29.4648 | 28.9231 | 28.4026 | 27.8819 | 27.3695 | 36.0033 | 35.4968 | 34.9583 | 34.4267 | 33.9142 | 33.3833 | 32.8711 | 32.3531 | 31.8292 | 31.2998 | 30.7649 | 30.2247 | 29.6793 | 29.1399 | 28.5844 | 35.9688 | 35.4035 | 34.8121 | 34.2058 | 33.5005 | 32.8755 | 32.226 | 31.5219
Field Capacity
Moisture Content, θFC
Crop is in stress
When moisture Content
is below this line!!

## Slide 61
Crop
Stress!

## Slide 62
Irrigation Application Rate and Timing

## Slide 63: Conclusion
Maintain soil water between
θFC and θt

## Slide 64: Gracias! For help with any of the methods covered in today’s presentation, please contact me by email at eric.harmsen@upr.edu